## Slide 1: ASTR 535
Observational Techniques
Instruments / Detectors
Introduction

## Slide 2: Instruments
What comprises an “instrument”?
  Detector
  Auxiliary optics, e.g.
    modifying shape of focal plane
    modifying image quality
    changing scale
    …
  Elements for spectral filtering, e.g.
    Filters
    Dispersing elements

## Slide 3: General considerations for optics
Location of optics: near focal plane vs near pupil
  Near focal plane won’t affect image quality
Throughput : transmission and reflection
Refractive vs reflective optics
  achromats

## Slide 4: Instrument example: field flattener
As previously noted, a typical telescope will have a curved focal plane (field curvature)
With a flat detector, focus cannot be achieved across the entire field
Can use a field flattener, near the focal plane, to shift the focus to a plane
As optic is near focal plane, neglible aberrations are introduced
Often built into detector dewar window

## Slide 6: ASTR 535
Observational Techniques
Instruments / Detectors
Focal plane and pupil reimagers

## Slide 7: Learning objectives
Understand why one might want a focal plane reimager
Understand the basic design and know the terminology collimator, camera lens, and field lens
Be able to determine how a reimager changes the scale, depending on the focal ratio of the camera lens
Understand why one might want to also reimage the pupil
Understand how a basic coronagraph works

## Slide 8: Focal plane reimagers
Motivation
  Change plate scale
    Focal reducer : demagnifies
    Focal expander : magnifies
  Access a collimated beam
  Access a pupil
Basic simple design
  Collimate light
  Refocus at different focal ratio
  Note light coming in on and off axis
This is a focal expander

## Slide 9: Pupil reimagers
Motivations
  Minimize size of optics
  Adaptive optics
  Coronagraphs
  IR instruments and cold pupil stops
Implementation: field lens
https://www.rp-photonics.com/field_lenses.html

## Slide 10: Coronograph
Used to image faint sources near bright ones
Basic design
  Focal plane mask to remove core of bright source (but diffraction wings remain)
  Pupil plane mask to remove wings

## Slide 11: IR cold stop
In IR, everything is glowing, including telescope and mirrors
Can’t block the part of the mirror that is reflecting light from the object, but can block the part that isn’t
But have to block it with something that isn’t emitting, i.e. something cold
Most IR instruments are cryogenic with a cold pupil stop to block thermal emission from the secondary

## Slide 12: Adaptive optics
In an AO system, pupil is imaged onto a deformable mirror, which corrects “aberration” from seeing in real-time
More later!

## Slide 14: ASTR 535
Observational Techniques
Instruments / Detectors
Filters

## Slide 15: Learning objectives
Understand basic terminology of filters and basic filter types
Understand implications of how interference filters work on their bandpasses

## Slide 16: Filters
classification by width: no standard definition, but roughly:
  Broad-band : > 1000 A
  Medium-band : 100-1000 A
  Narrow band : < 100 A
Classification by type
  Colored glass
  Interference filters

## Slide 17: Colored glass filters
Work due to absorption/transmission of various pigments
Wide variety of glasses have been developed (e.g., Schott, Hoya, etc.)
Bandpasses constructed by different combinations of glasses, e.g from Bessell 1979:

## Slide 18: Interference filters
Uses partially reflective dielectric coatings to set up interference
Constructive interference occurs at
mλ = 2nd cosθ
Achieve desired bandpass by adjusting n and d, amount of reflection, use multiple layers
  Allows for highly customized bandpasses, with sharp cutoffs
Note also antireflection coatings
Ordered: r I u g z

## Slide 19: Interference filter bandpasses
mλ = 2nd cosθ
 bandpass depends on angle of incidence (AOI)
Implication:
Interference filter in collimated beam
  Angle of incidence corresponds to field angle!
  Filter bandpass shifts with field angle
Interference filter in converging beam
  All field angles have range of angles of incidence
  Filter bandpass broadens compared to zero AOI
Spectrodon calculator

## Slide 21: ASTR 535
Observational Techniques
Instruments / Detectors
Fabry-Perot interferometers

## Slide 22: Learning objectives
Know the principles of how a Fabry-Perot interferometer works and how they are used in astronomy

## Slide 23: Imaging spectroscopy: Fabry-Perot interferometer
the etalon: a tunable interference filter
  Tuned by changing index of refraction (pressure), tilt
Location of etalon in collimated beam
  Implication: different bandpass at different field angle

## Slide 24: Fabry-Perot data cubes
Take stack of images, scanning through etalon spacings
Constant wavelength is a paraboloid through the stack
Analysis can be complex, depends on stable conditions
Usually done in narrow bandpass, e.g. for kinematics, but there are some etalons at lower spectral resolution

## Slide 26: ASTR 535
Observational Techniques
Instruments / Detectors
Dispersing spectrographs

## Slide 27: Learning objectives
Understand the basic principles of how a dispersive spectrograph works
Understand the basic functions of the slit, collimator, dispersing element, and camera lens
Be able to draw a spectrograph schematic and draw rays of different wavelengths through the system
Understand the terms dispersion and resolution, and know what they depend on

## Slide 28: Dispersing spectrographs
Basic design
  Focal plan reimager, with a dispersing element
  Dispersing elements:
    Diffraction grating: transmission or reflection
    Prism

## Slide 29: Spectrographs
Consider spectrograph as an imager with dispersion
Note potential confusion of sources!
Slit spectrograph

## Slide 30: Spectrographs
Consider spectrograph as an imager with dispersion

## Slide 31: Important user characterization of a spectrograph
Three important characteristics:
  Dispersion: how much light is spread as a function of wavelength
  Resolution: how well can you resolve different wavelengths
  Throughput: how much light is recorded

## Slide 32: Dispersion
Dispersion gives the amount that the light is dispersed
  Angular dispersion (angle per wavelength, e.g. radians/A), d𝜃/d𝜆
  Linear dispersion (distance in focal plane per wavelength e.g. mm/A), dx/d𝜆
  Astronomers typically call the inverse linear dispersion the dispersion (wavelength per distance, e.g. A/mm or A/pixel)
  “high” dispersion means light is more spread out, i.e. less A/pixel
Angular dispersion depends on the nature and details of the dispersing element
Linear dispersion depends on the dispersing element, but also on the focal length of the camera lens (since that sets the “scale”)

## Slide 33: Resolution
Resolution describes how well one can separate features at different wavelengths
  Alternatively, how broad is a monochromatic feature
Recall, a spectrograph is an imager with a dispersive element
  A monochromatic source looks like the source
Width of a monochromatic feature is given by the size of the source
  Without a slit, depends on the seeing
  With a slit, depends on the width of the slit
    where r is the anamorphic magnification, which is a magnification result from the dispersing element in the direction of dispersion
Schroeder, Astronomical Optics

## Slide 34: Descriptions of resolution
Resolution can be described in several ways
  width of a monochromatic source, related to physical slit width by magnification of spectrograph (including anamorphic magnification)
  Dimensionless resolution: =
Resolution may be a function of wavelength depending on the dispersing element
  If is constant with , then R won’t be, and vice versa
Schroeder, Astronomical Optics

## Slide 35: Throughput
Throughput gives amount of light through spectrograph
one factor is the nature of the dispersing elements, but also the transmission of the optics, which are often more complicated than the simple picture!
The narrower the slit, the lower the throughput: tradeoff between resolution and throughput
  Typically slit is set around the width of seeing disk, so that resolution doesn’t vary between exposures
  For spectrophotometry, a wider slit is often used
  Remember differential refraction, where throughput may be a function of wavelength if the slit is not aligned with the parallactic angle!

## Slide 37: ASTR 535
Observational Techniques
Instruments / Detectors
Types of astronomical spectrographs

## Slide 38: Learning objectives
Understand different types of astronomical spectrographs:
  Slitles spectroscopy
  Long-slit spectroscopy
  Slitlet spectroscopy
  Fiber-fed spectroscopy
  Integral field spectroscopy
  Echelle spectrograph

## Slide 39: Slitless spectroscopy
Yields spectra of all objects in field
Implications for overlap : generally used for very low dispersion, so that each object produces a relatively “short” spectrum
  Often implemented using a “grism”
  Historically, implemented with objective prism spectroscopy
Implication for sky background

## Slide 40: Long slit spectra
To avoid overlapping spectra, add an entrance slit to the spectrograph
Produces spectra along a line in the sky

## Slide 41
Spectroscopy with slitlets
Long slit spectrograph gives spectra along a line
For many projects, objects won’t lie along a line
Can observe more objects using slitlets
Note possible implication for wavelength coverage
Slit mask needs to be constructed for each field in advance
JWST is pioneering a “programmable” slit mask

## Slide 42: Multiobject spectroscopy with fibers
Alternatively, if objects don’t fall along the line, line them up!
Use optical fibers to take objects from different parts of the field and “line them up” along a slit of a spectrograph, or let the fiber ends themselves make up a “pseudo-slit”
Again, fibers need to be positioned for a specific field
SDSS APOGEE spectrograph

## Slide 43
Robotic fiber positioners

## Slide 44
Integral field (3D) spectroscopy
For an extended object, ideal would be to get spectra at all location in the object, not just along a line  integral field spectroscopy
Several implementations:
  Lenslets
  Fibers
  Image slicer
https://www.dur.ac.uk/cfai/spectroscopy/introductiontointegralfieldspectroscopy/

## Slide 45: Echelle spectrograph
If you want to work at high dispersion/resolution, and also cover a large wavelength region, you have a problem, as you would need a very wide detector
An alternative way to achieve this is to use an echelle spectrograph, which uses a diffraction grating operating at high order to generate a series of spectra covering different wavelength ranges, and then cross-disperses these with a second dispersing element to put them onto a detector
With an echelle, all of the detector is used for a single object!

## Slide 47: ASTR 535
Observational Techniques
Instruments / Detectors
Dispersing elements

## Slide 48: Learning objectives
Understand the basics of how prisms and diffraction gratings work
Understand the grating equation and how dispersion depends on order and groove/line spacing
Understand grating orders and order overlap, and how it is handled
Understand how an echelle spectrograph works
Understand some basics of factors that affect grating efficiency

## Slide 49: Dispersing elements : prism
Prisms disperse light because index of refraction of glasses is a function of wavelength
where t is base length, and d is input beam diameter
Generally relatively low resolution compared to gratings
Used, e.g., for objective prism spectroscopy and for cross dispersing in echelle spectrograph; also in grisms
PASP 129,976
Schroeder, Astronomica Optics

## Slide 50: Diffraction gratings
multi-slit interference (note this is not spectrograph slit!)
Simplest: alternating grooves (lines) spaced by 𝜎, either reflective or transmissive
Grating equation: constructive interference:
)
dispersion: more dispersion at higher order
  more dispersion at higher 𝛼 and 𝛽 (echelle)
Typical gratings have groove densities between 300 and 1200 lines/mm
At given configuration, more lines/mm (smaller spacing) gives higher dispersion and resolution, proportional to lines/mm
Schroeder, Astronomica Optics

## Slide 51: Orders and order overlap
Light from different orders can fall at same location
more overlap at higher orders
Use order-blocking filter (common for low order) or cross-dispersion (common for high order)

## Slide 52: Echelle spectroscopy
Echelle spectrographs work at multiple high orders and cross disperse
Note that light of a given wavelength can appear in multiple orders

## Slide 53: Grating throughput/efficiency
Gratings can be constructed to direct light into particular orders by “blazing” the grating, i.e. tilting the reflective facets (also removes need for dark areas in between)
Typical grating efficiency around 50-70 percent
New technology called volume phase holographic (VPH) gratings allows higher throughput in a transmission grating
  Varies index of refraction on very small scales
conventional
VPH

## Slide 55: ASTR 535
Observational Techniques
Instruments / Detectors
More spectrographs

## Slide 56: Learning objectives
Recognize connection between spectrograph resolution and ability to get velocity information
Be aware of some possibilities for non-dispersive spectroscopy

## Slide 57: Resolution and capability
Resolution can be described by the dimensionless resolution
Typical dispersive spectrographs have resolution between R=1000 (low dispersions), R=30000 (typical echelles) and R=100,000 (high precision RVs)!
Note that this is closely related to the velocity resolution, since
= =
R= 1000  = 300 km/s
R=100000 --> = 3 km/s
an astrophysical velocity width (e.g. velocity dispersion) might be measurable down to 0.1-0.5 of the spectrograph resolution
An astrophysical velocity centroid (e.g., radial velocity) might be measurable to 0.01-0.1 of the spectrograph resolution, and even better if multiple features are being measured

## Slide 58: Non-dispersive spectroscopy
We’ve described multiple types of spectrographs that use dispersing elements
We’ve also described the Fabry-Perot interferometer, which provide spectroscopic capability through a tunable filter
It’s also possible to get spectroscopic information through interferometry, i.e. combining light from an object to produce fringes, since interference is a function of wavelength
Fourier transform spectrograph: splits beam into two parts, changes path length of one arm and records interference pattern (essentially a Michaelson interferometer)
  Record fringe pattern as a function of path spacing, use it to recover spectrum
  FTS can provide very high resolution, typically for very bright sources
Mach–Zehnder interferometer, e.g. JIVE
Schroeder, Astronomical Optics

## Slide 60: ASTR 535
Observational Techniques
Instruments / Detectors
Detectors

## Slide 61: Learning objectives
Understand the basic principles of detectors
Understand the difference between photon counting and photon collecting devices
Understand terminology used to describe detector characteristics: quantum efficiency, detector resolution, readout noise, pattern noise, dark current, linearity

## Slide 62: Detectors
Basic types:
  Photographic
    Chemical reactions to light
  Photoelectric detectors
    Photoelectric effect: photons have energy E=h that can excite electrons in a material
    Wavelength sensitivity depends on photosensitive material : minimum excitation energy and cross-section
    Two general classes:
      Photon counters
      Photon collectors

## Slide 63: Photon counters
Photons make “events” that are counted in real time
  Photomultipliers
    Avalanche photo diodes (APD)
  Photon counting arrays
    Multi-anode microchannel arrays (MAMAs)
Since an event is counted after amplification there is no associated readout noise
Can time-tag photons

## Slide 64: Photon collectors
photons generate photoelectrons, which are collected and subsequently read
Different materials:
  Si (optical to about 1 micron)
  HgCdTe, InSb, PtSi, used in near IR
Different readout electronics: CCD, CMOS, IR multiplexer

## Slide 65: Detector characteristics
Quantum efficiency : fraction of incident photons that are detected
  Photographic ~1%
  Photon counter: tens of percents
  Photon collectors: 50-90 %
Of course, QE is a function of wavelength
Increasing QE is equivalent to increasing telescope aperture!

## Slide 66: Detector characteristics
Size / resolution elements
  Physical size related to maximum field-of view
  With reimaging optics, number of spatial resolution elements, i.e. number of pixels, is more relevant
  Modern detectors have many megapixels, typical in astronomy 1024x1024, 2048x2048, 4096x4096, typically smaller in the near-IR than in the optical
  Commercial detectors have even more, but not all are available for astronomical applications, i.e. high sensitivity and low noise
  Arrays of detectors possible, typically with some gap, e.g. DECAM
A common figure of merit for surveys is
discovery efficiency = size * QE

## Slide 67: Detector characteristics
Readout effects
  Readout noise : random, Gaussian noise introduced in the readout process: typically few electrons rms
  Pattern noise :
    Non-random, i.e. spatially correlated noise that is sometime present in detector/signal chains (e.g. with 60 Hz pattern)
    Fixed pattern noise is pattern noise that is repeatable in time, i.e. potentially correctable, e.g. with bias frames
      Much pattern noise is not fixed pattern noise!
Photon counting devices aren’t subject to readout noise!
KOSMOS bias frames

## Slide 68: Detector characteristics
Dark current : electrons generated from thermal excitation (not photoelectrons)
  Larger at higher temperatures
  Larger for detectors with lower excitation energy (i.e. IR detectors)
Mitigated by cooling detectors
  Most optical detectors cooled cryogenically to somewhere between -120 and -70 C, typically with LN2 (-196 C)
  IR detectors cooled more, e.g. liquid He (4K!)
  Lower cost detectors cooled thermoelectrically, typical amateur camera cools to 30-50 C below ambient  still significant dark current, e.g. TMO
Dark current can be corrected by dark frames, but note that calibration frames have both Poisson and readout noise

## Slide 69: Detector characteristics
Linearity : relation between input photons and output photoelectrons
  Slope is QE
  Linear detector means slope is independent of count level
Full well : maximum number of photoelectrons in device
A/D saturation: maximum count level, determined by number of bits in A/D
TSPEC
ARCTIC
DIS

## Slide 70: Other detector characteristics
Defects, e.g. bad pixels, bad columns, etc.
Modulation transfer function
  fringing
Readout speed
Saturation behavior
Hysteresis
reciprocity

## Slide 72: ASTR 535
Observational Techniques
Instruments / Detectors
Digitization

## Slide 73: Digitization
Although we talk about detectors collecting individual photoelectrons, the electronics that sense this produce analog output (voltages)
This is converted to a data number (DN) by a device called an analog-to-digital (A/D) converter
A/D converters work by comparing the input voltage to a series of reference voltages and setting bits depending on the comparison
The range of numbers that can come out of an A/D converter depends on how many reference voltages there are:
  12-bits : 0-4095 (2**12)
  16-bits : 0-65535
  18-bits: 0-262143

## Slide 74: Dynamic range
Ratio of brightest to faintest things you can measure in a single exposure
Certainly limited by A/D
Additionally limited by readout noise - at low levels your measurement is limited by noise
At high level, may be limited by non-linearity, if detector goes nonlinear before A/D saturation

## Slide 75: Gain
Digital detector signal chains usually introduce an electronic “gain”: a multiplicative constant that modifies the signal coming from the detector before the signal is digitized
Because of this, the data numbers do not directly give the number of detected photons (each of which generates an electron)
Instead
N(electrons) = GC
where C is the number of counts (DN) and G is the “gain” in “units” of electrons/DN (all dimensionless), even though an electronics person would call this the ”inverse gain”
Knowing the gain is critically important, because the Poisson statistics is determined from the number of detected photons, not the DN value

## Slide 76: Gain and Poisson noise
N(electrons) = GC
So the noise in electrons is:
𝜎 (electrons ) = =
Usually, however, people don’t convert images to units of electrons (although some do!)
In units of counts:
C =
So
𝜎 (counts) = =
Note that S/N doesn’t change if you were to change the gain, because the number of counts would change as well!

## Slide 77: Determining the gain and readout noise
Covered previously!
As a reminder these are determined from the measurement of noise properties:
  For gain, take difference of two images at a high light level, determine the variance, and compare with mean level to determin gain
  𝜎 (counts in difference image) =
  Difference images are used to avoid variance from difference in pixel sensitivities
  For readout noise, take difference of two images at zero light level (biases), determine the variance:
  𝜎 (counts in difference image) =
  More comprehensive test determines variance at a range of light level: tests understanding of noise model and help to detect nonlinearities

## Slide 79: ASTR 535
Observational Techniques
Instruments / Detectors
Optical detectors

## Slide 80: Learning objectives
Understand the basics of how CCDs work
Under the concept of charge transfer efficiency
Learn about electron multiplying CCDS
Learn about CMOS detectors and how they compare with CCDs

## Slide 81: Optical photon collectors
Generally use silicon as the photosensitive material
Si band-gap leads to cutoff wavelength ~1.1 microns

## Slide 82: Charge Coupled Devices (CCDs)
Readout method
Charge transfer issues
  Charge transfer efficiency (CTE)
    CTE must be very close to unity, e.g.
    .999**2048=.128 !
    .9999**2048 = 0.815
    .99999**2048 = .9797
  Note issue of CTE degradataion in space environment
  Deferred charge and preflash
binning

## Slide 83
  Front side vs back side illumination
  Fringing
CCD QE
Spectrograph fringing (DIS)
Imaging fringing

## Slide 84: Electron multiplying CCDs (EMCCDs)
Electronics includes an extra “multiplication”, allowing readout noise to be negligible, i.e. approximating a photon counting device
Possible negative factors
  Extra noise factor at higher count rates
  Smaller dynamic range
https://andor.oxinst.com/learning/view/article/electron-multiplying-ccd-cameras

## Slide 85: CMOS detectors
Complementary metal oxide semiconductor
Readout method
Readout speed
  CCDs trade speed for readout noise
  CMOS much faster
Pros/cons vs CCDs
  Dynamic range (A/D)
  cost
https://andor.oxinst.com/learning/view/article/comparing-scmos

## Slide 87: ASTR 535
Observational Techniques
Instruments / Detectors
IR detectors

## Slide 88: Learning objectives
Learn about typical materials used for detection of near-IR photons
Understand how the readout of near-IR detectors is different from that of optical detectors: non-destructive readout, resets, and KTC noise
Understand readout modes of near-IR detectors: doubly correlated sampling, Fowler sampling, up-the-ramp sampling

## Slide 89: IR detectors
Materials
  HgCdTe (“mercury-cadmium-telluride, mer-cad-tel”) to 2.5 micron (can be tuned to lower)
  InSb (“indium antimonide”, “insby”): to 5 microns
Photosensitive material is linked to readout material (the “multiplexer”)

## Slide 90: IR detector readout
IR multiplexers can be read without affecting the accumulated photoelectrons: ”non-destructive” readout
  Readout noise typically larger than than of optical devices
Pixels are “reset” separately
  Reset process resets “zero” level, but with some associated noise (“KTC” noise), which is substantial
  Accounting for this requires different readout modes than for optical devices

## Slide 91: Readout modes
Reducing readout
  Doubly correlated sampling: read twice, once after reset, then again after exposure time. Difference the images
  Fowler sampling: read multiple times after reset, then multiple times after exposure time
  Up the ramp sampling: read continuously and fit slipe

## Slide 93: ASTR 535
Observational Techniques
Instruments / Detectors
UV detectors

## Slide 94: UV detectors
Because of low background, photon counting devices are often preferred