## Slide 1: ASTR 535
Observational Techniques
Fall 2019 (10/23)
Instruments / Detectors

## Slide 2: 11/2
Questions
Imaging data reduction
  World coordinate systems
  Running notebooks remotely

## Slide 3: 11/7
Questions
Discussion
Imaging data reduction

## Slide 4: 11/9
Questions
Discussion
  Fibers
Different types of spectrographs : data
  Data puzzles
Imaging data reduction

## Slide 5: 11/14
Questions
Discussion
Spectrographs
  Imagine someone said they were building a new spectrograph for the 3.5m. What performance information would you like to know about it to assess its scientific capabilities?
  Canvas: Spectrograph resolution

## Slide 6: 11/16
Questions
Discussion
Detectors
  Basic principles
  Characteristics
  Digitization
  Optical and IR detectors
KOSMOS : measuring the gain and dispersion

## Slide 7: 11/28
Discussion/questions
Final
IR observing and data reduction
Similar techniques in the optical for faint objects
  Dithering
  Nod and shuffle
KOSMOS : measuring the gain and dispersion
IR data inspection: TSPEC slit viewer

## Slide 8: 11/30
Discussion/questions
Final
Measuring the gain
Spectroscopy data reduction demo:
  KOSMOS
  ARCES
  TSPEC

## Slide 9: Instruments
General considerations
  Location of optics: near focal plane vs near pupil
  Throughput : transmission and reflection
  Refractive vs reflective optics
    achromats

## Slide 10: Instrument examples
Field flatteners
Focal plane reimagers
  Why?
Pupil reimagers
  Field lens
  Motivations
    Adaptive optics
    Minimize size of optics, e.g. https://www.rp-photonics.com/field_lenses.html
    Coronagraphs
    IR instruments and cold pupil stops

## Slide 11: Filters
classification by width
  Broad-band
  Medium-band
  Narrow band
Classification by type
  Colored glass
  Interference filters: partially reflecting parallel surfaces
    mλ = 2nd cosθ
    Dependences on angle of incidence: implication for filter location and bandpass variation in different optical systems (c.f. Coronado solar telescopes)
    Note also antireflection coatings

## Slide 12: Imaging spectroscopy: Fabry-Perot interferometer
the etalon: a tunable interference filter
  Tuned by changing index of refraction, tilt
Location of etalon in collimated beam
  Implication: different bandpass at different field angle
Fabry-Perot data cubes

## Slide 13: Dispersing spectrographs
Basic design
  Focal plan reimager, with a dispersing element
  Dispersing elements:
    Diffraction grating
    Prism
Basic spectrograph user characteristics
  dispersion
    Angular dispersion (angle per wavelength, e.g. radians/A) : dispersing element
    Linear dispersion (distance per wavelength e.g. mm/A) : dispersing element + camera lens
    Inverse linear dispersion (wavelength per distance, e.g. A/mm or A/pixel)
  resolution
  throughput

## Slide 14: Spectrographs
Consider spectrograph as an imager with dispersion
Note potential confusion of sources!
Slit spectrograph
Resolution of a spectrograph
  Dependence on slit / image width
  Numerical description
    width of a monochromatic source, related to physical slit width by magnification of spectrograph (including anamorphic magnification)
    Dimensionless resolution:
  roughly constant at fixed order of dispersive element

## Slide 16: Astronomical spectrographs
Slitless spectroscopy
  E.g. grism
  Implication for sky background
Long-slit spectroscopy
multiobject spectroscopy with slitlets
Image slicers:
Fiber spectrographs
Integral field spectrograph

## Slide 20: Dispersing elements
Prisms
Diffraction gratings: multi-slit interference (note this is not spectrograph slit!)
  Grating equation
    mλ = σ(sinβ + sinα)
  Orders and order overlap
  Echelle spectroscopy
  Anamorphic magnification
  Grating throughput/efficiency and grating blaze
    Volume phase holographic (VPH) gratings

## Slide 21: Detectors
Basic types:
  Photographic
  Photoelectric detectors
    Photoelectric effect
    Photon counter: photons make “events”
      Photomultipliers
      Photon counting arrays
    Photon collector: photons generate photoelectrons
      Different materials: Si, HgCdTe, InSb, PtSi
      Different readout electronics: CCD, CMOS, IR multiplexer

## Slide 22: Detector characteristics
Quantum efficiency
Size / resolution elements
Discovery efficiency : size * QE
Readout effects
  Readout noise
  Pattern noise / fixed pattern noise
Dark current
Linearity
Full well

## Slide 23: More detector characteristics
Others
  Defects
  Modulation transfer function
    fringing
  Readout speed
  Saturation behavior
  Hysteresis
  reciprocity

## Slide 24: Digitization
A/D converters: bits and output range
Gain/amplification
  Implication for noise calculations
Dynamic range
Determining gain and readout noise
  Single frame: = C G +
  But there can be variations of L across frame, so can’t do spatial statistics to get variance; could take lots of frames and get statistics on a per pixel basis, or …
  Use difference between pair of frames
  Low and high light level for rn and gain, respectively, or, better yet, range of light levels to verify expected noise performance

## Slide 25: CCDs
Readout method
Charge transfer
  CTE
  Deferred charge
binning
QE
  Front side vs back side thinned

## Slide 26: CMOS detectors
Complementary metal oxide semiconductor
Readout method
Readout speed
Pros/cons vs CCDs

## Slide 27: IR detectors
Readout method: multiplexer
Non-destructive readout
Reset (kTC) noise
Readout noise
Readout modes
  Doubly correlated sampling
  Fowler sampling
  Up the ramp sampling

## Slide 28: UV detectors
Because of low background, photon counting devices are often preferred